## Slide 1
EagleEye: Intelligent Edge AI Surveillance System
Mid-Project Evaluation
[Member 1], [Member 2], [Member 3]
[Advisor Name]
[Date]

## Slide 2
Problem Statement (Recap)
The Issue: Traditional surveillance systems are bandwidth-heavy, expensive, and privacy-invasive (streaming 24/7 video to the cloud).
The Gap: Lack of affordable, "privacy-first" smart cameras that process data entirely on the edge.
Our Goal: Develop a decentralized, low-power surveillance system that detects intruders locally on an ESP32-CAM and only transmits confirmed threats.

## Slide 3
Proposed Solution & Core Functionalities
Project Concept: A proactive, multi-layered security system combining Edge AI with physical automation.
Key Functionalities:
AI Vision Detection: Real-time human recognition using TinyML (eliminating simple motion false alarms).
Voice Alert System: Immediate audible warnings (Text-to-Speech/Siren) upon detection to deter intruders.
Smart Arming Logic: Automated "Arm/Disarm" triggers based on sensor states.
Live Surveillance: Low-latency video streaming for manual verification.
Dynamic Camera Control:
  Auto: Intelligent tracking of moving targets.
  Manual: Remote Pan/Tilt control via the mobile app.
Physical Security: Integrated Remote Door Lock control to secure premises instantly.
The Solution:
Bridging the gap between passive CCTVs and expensive smart security.
Providing a system that detects, acts, and secures autonomously.

## Slide 4
Previous Literature Review Findings
Commercial & Cloud-Centric Limits:
  Systems (Ring/Nest): Rely on continuous cloud streaming, causing high bandwidth usage and privacy risks (data stored externally) [1].
  Cost & Power: Recurring subscription fees and high power consumption (~1.25V/hour) make them unsuitable for off-grid use.
Early Edge AI Limitations:
  Complex Models: Standard architectures like MobileNet-SSD or YOLOv5 are too heavy for ESP32, causing low frame rates (1–3 FPS) and high latency.
  Hardware Failures: Large tensors exhausted the 520KB SRAM, leading to frequent "Brownout" and "Camera Init Failed" errors.
  Sensor Reliability: Reliance on simple PIR sensors caused 85-95% false positive rates (triggered by wind/animals).

## Slide 5
Current Literature & TinyML Advancements
Quantization Revolution:
  Technique: Converting 32-bit floating-point weights to 8-bit integers (Int8).
  Result: Reduces model size by ~75% while retaining ~97% detection accuracy, allowing fit within limited SRAM.
Optimized Custom Architectures:
  Grayscale Inputs: shifting from RGB to 1-channel (48x48) inputs reduces tensor interactions by 3x.
  Shallow CNNs: Custom layers designed for specific object detection (Human) outperform generic "Kitchen Sink" models in speed (~112ms inference).
Energy & Architecture:
  Sensor Fusion: Waking the camera only on PIR triggers reduces idle consumption (~0.93V/hour).
  Frameworks: TensorFlow Lite for Microcontrollers enables OS-free, low-latency inference on bare metal.

## Slide 6
System Architecture — v1: Local Prototype (LAN-only)
▦ [Diagram Request: 3-zone flat diagram — SITE (ESP32-CAM) → SITE PC (Mosquitto broker + bridge.py → Cloudinary/Firebase) → Phone (same LAN). Mark live-video & servo as ❌ camera-LAN-IP links.]
One network for everything; a PC had to stay powered on at the site.
Flow: ESP32-CAM → local Mosquitto broker on a site PC → `bridge.py` uploads the JPEG to Cloudinary + writes alert metadata to Firebase → app reads Firebase.
Live video & servo: the app talks directly to the camera's LAN IP (HTTP MJPEG / GET /servo).
Arm / disarm: app → Firebase config/armed; the bridge gates on it.
Limitations: ❌ same network only · ❌ a PC must stay on running Mosquitto + bridge.py · ❌ type the camera's IP (breaks on CGNAT / no port-forwarding) · ❌ open broker, no TLS, hardcoded Wi-Fi creds → not shippable.
Notes: Visuals to add:
- [Diagram Request: 3-zone flat diagram — SITE (ESP32-CAM) → SITE PC (Mosquitto broker + bridge.py → Cloudinary/Firebase) → Phone (same LAN). Mark live-video & servo as ❌ camera-LAN-IP links.]

## Slide 7
System Architecture — v2: Cloud & Outbound-Only (HiveMQ + Relay) ★ current
▦ [Diagram Request: 3-zone flat diagram — SITE A (ESP32-CAM, any network / 4G) → CLOUD (HiveMQ Cloud MQTT broker · Cloudinary · Firebase → Cloud Function → FCM · Deno Deploy WS relay) → ANYWHERE (Phone). All device arrows point OUTWARD (teal); 🔒 lock on every link.]
The device dials out to the cloud and stays connected — so it works from any network with no IP, no port-forwarding, no PC on site.
Outbound-only rule (the key idea): the camera always connects out and stays connected, like a messaging app → no static IP, no port-forwarding, no on-site PC.
Control + alerts plane: MQTT over TLS to HiveMQ Cloud (managed broker). Topics status (with LWT → true online/offline), alert, cmd (servo, arm/disarm, stream on/off), cmd/ack. The app speaks MQTT-over-WebSocket — servo & arm/disarm work from anywhere.
Alerts anywhere: device HTTPS-POSTs the JPEG directly to Cloudinary, writes metadata to Firebase → a Cloud Function fires an FCM push → phone is alerted even with the app closed. (No bridge.py, no site PC.)
Video plane (on-demand): app sends cmd:{stream:on} → device opens an outbound WebSocket to the Deno Deploy relay → relay fans frames to the app; closing the screen stops it. Never 24/7 (QVGA–VGA JPEG, ~5–15 fps).
Security & cost: TLS everywhere (mqtts 8883 / wss / HTTPS), per-device credentials, least-privilege topics; works on Wi-Fi / office / 4G-LTE; entire stack on free tiers (~$0–10 / month).
Notes: Visuals to add:
- [Diagram Request: 3-zone flat diagram — SITE A (ESP32-CAM, any network / 4G) → CLOUD (HiveMQ Cloud MQTT broker · Cloudinary · Firebase → Cloud Function → FCM · Deno Deploy WS relay) → ANYWHERE (Phone). All device arrows point OUTWARD (teal); 🔒 lock on every link.]

## Slide 8
Engineering Design: The Edge Layer
▦ [Visual Request: Photo of ESP32-CAM setup]
Hardware: AI-Thinker ESP32-CAM.
Workflow:
  Capture: Frame (RGB565).
  Pre-processing: Center-crop & resize to 96x96 RGB, normalize to [0,1] (matches the deployed v7.16 model).
  Inference: Run the custom from-scratch depthwise-separable TFLite Micro INT8 model.
  Logic: If human probability exceeds the alert threshold -> Trigger Alert state.
Innovation: Implemented "Warm-up" and "Cooldown" state machines to prevent false positive loops and sensor noise.
Notes: Visuals to add:
- [Visual Request: Photo of ESP32-CAM setup]

## Slide 9
AI Vision — Model Evolution
▦ [Visual Request: Horizontal 5-phase timeline plotting Accuracy vs Latency, ending at the ★ v7.16 marker]
Governing constraint: the detector must run on the ESP32-CAM itself — ~100 kB tensor arena, no GPU, no cloud inference, sub-second latency. Every version is a negotiation between accuracy, latency, memory, and real-world reliability. 17 engineered variants (v1.0 → v7.17) across five phases — the recurring lesson: the smallest model is not the best model; converge on the smallest model that still generalizes.
Phase 0 — Off-the-shelf reference (Oct–Dec 2025): bootstrapped on pre-built person detectors (Edge Impulse + a TFLite ESP32 reference). Proved the on-device TFLite pipeline works (first end-to-end IoT path ~712 ms). Lesson: inference works on-device, but a generic model is slow and not ours.
Phase 1 — Custom "Tiny CNN", 48×48 grayscale (Feb–May 2026): trained our own. v1.0 baseline (~80–85%, ~106 ms) → v1.1 color reverted (latency/memory) → v2.0 augmented → v2.1 hard-negative >90% (live ESP32 capturer) → v3.0 Optuna-heavy 94.96% but >300 ms → v4.0 knowledge-distilled 91.77% @ <150 ms → v5.0 tiny-dropout 91.7%, 12.6 KB. Lesson: accuracy is available, but not for free.
Phase 2 — Edge Impulse cloud, 48×48 (mid-May 2026): EI project 1000575 "final", ~1,862 images. v6.0 RGB (superseded — firmware fed 1-channel) → v6.1 grayscale (long-running deployed EI model). Firmware lesson: AllOpsResolver → MicroMutableOpResolver (register only needed ops).
Phase 3 — Transfer learning: MobileNetV1 0.2, 96×96 RGB (mid-May–Jun 2026): the 48×48 grayscale tiny CNN couldn't generalize in real scenes. Jumped to a pretrained MobileNetV1 backbone — with ESP-NN (Espressif's optimized neural-network kernel library that accelerates TensorFlow Lite Micro inference on the ESP32) disabled, because it produced saturated/wrong predictions for the MobileNet path on the ESP32-S1. Sweep v7.0 (89.86%) → v7.3 class-weighted = 92.35% test (project peak) → v7.4 64×64 + EON 91.13% / ~570 ms (fast pick). Findings: resolution > color; 48px collapses recall; 0.1-width can't reach 90%.
Phase 4 — From-scratch depthwise-separable → the final model (late May–Jun 2026): for the FYP novelty we wanted a custom, from-scratch model still >90%. Standard from-scratch convs (v7.11–v7.13) overfit (recall 67–76%). Breakthrough = depthwise-separable convolutions (~8–10× fewer MACs): v7.14 gray80 (86.85%, but an ESP-NN depthwise-kernel bug saturated it → "always human") → v7.15 rgb80, ESP-NN off (bias fixed, balanced 88.38%) → ★ v7.16 rgb96, ESP-NN off: 90.83% test, 87.5% human recall, balanced, ~872 ms — the deployed final model. v7.17 is the grayscale sibling (86.24%, below target).
Phase 5 — In-house local pipeline (13 Jun 2026): a local replica of the EI "final" CNN (model-training/train_rgb.py) so the team owns the whole train → quantize → model_data.h → flash loop. RGB 92.16% INT8; grayscale 91.83% (with 100 pure-black frames added as non-human negatives so a blacked-out camera reads non-human).
Model evolution — at a glance (latency = on-device ESP32-CAM; `` = estimated / not separately benchmarked):*
¹ Held-out test accuracy, INT8, unless noted (v3.0 = 5-fold CV; v1.0 / v6.1 ≈ validation). ² On-device ESP32-CAM; * = estimated. ³ INT8 validation (local pipeline). Full per-version log: models/MODEL_VERSIONS.md.
Ver. | Architecture | Input | Trained on | Accuracy¹ | Latency² | Verdict
P0 ref | Pretrained person detector (EI / TFLite) | ~96×96 | COCO-person (pretrained) | — | ~700 ms* | proved on-device TFLite; generic, not ours
v1.0 | Tiny separable CNN | 48×48 gray | ~1.5k human / non-human* | 80–85% | ~106 ms | original prod; too weak
v2.1 | Tiny CNN + hard-negatives | 48×48 gray | + live field hard-negatives | >90% | ~106 ms | field-hardened
v3.0 | Heavy CNN 16-32-64 (Optuna) | 48×48 gray | same set, 5-fold CV | 94.96% | >300 ms | most accurate, too slow
v4.0 | Distilled tiny (MobileNetV2 teacher) | 48×48 gray | distillation set | 91.77% | <150 ms | fast, but 48px ceiling
v6.1 | Edge Impulse CNN | 48×48 gray | EI cloud ~1,862 imgs | ~90% | ~110 ms* | long-deployed; detail-limited
v7.3 | MobileNetV1 0.2 (transfer) | 96×96 RGB | cleaned 469h / 920n + class-wt | 92.35% (peak) | ~1 s* | most accurate (borrowed backbone)
v7.4 | MobileNetV1 0.2 + EON | 64×64 RGB | same cleaned / balanced | 91.13% | ~570 ms | fast pick
v7.15 | Depthwise-separable, from-scratch | 80×80 RGB | balanced 929h / 920n | 88.38% | ~750 ms* | bias fixed; just under 90
★ v7.16 | Depthwise-separable, from-scratch | 96×96 RGB | balanced 929h / 920n | 90.83% | ~872 ms | deployed final
v7.17 | Depthwise-separable (gray) | 96×96 gray | balanced 929h / 920n | 86.24% | ~820 ms* | lower-RAM sibling
Local-RGB | From-scratch (EI replica, train_rgb.py) | 96×96 RGB | balanced 763 / 763 | 92.16%³ | ~872 ms* | in-house pipeline
Local-gray | From-scratch (+100 black frames) | 96×96 gray | balanced 763 / 763 + black | 91.83%³ | ~820 ms* | currently flashed
Notes: Visuals to add:
- [Visual Request: Horizontal 5-phase timeline plotting Accuracy vs Latency, ending at the ★ v7.16 marker]

## Slide 10
AI Vision — Training Techniques (the toolbox)
Across the evolution, each phase contributed a reusable technique. The key ones:
INT8 post-training quantization — 32-bit floats → 8-bit integers (~4× smaller, fast integer math on the MCU) via representative-dataset calibration. Exposed a real "quantization gap" (float ↑ but INT8 flat — v7.1) that later phases had to close.
Data augmentation — RandomFlip / Rotation / Zoom / brightness jitter for robustness to lighting and camera angle (v2.0+).
Hard-negative mining — a live ESP32 Wi-Fi capturer harvested the exact false positives/negatives the camera saw in the field; oversampled them to push past 90% (v2.1). Train on what the device actually gets wrong.
Optuna hyperparameter search — automated tuning of learning rate, dropout, and architecture (v3.0: 94.96% F1; also tuned the distillation in v4.0).
Knowledge distillation — a large MobileNetV2 teacher transferred its learned probabilities into a tiny student (α = 0.378, T = 9.23) → 91.77% @ <150 ms (v4.0).
Class balancing — geometric augmentation to parity (v7.2) vs class weighting / cost-sensitive learning (v7.3, the winner) — fixed the human-minority bias on cleaned data.
Transfer learning — a pretrained (ImageNet) MobileNetV1 backbone, width 0.2, 96×96 RGB (v7.0–v7.9) — reached the project's peak accuracy of 92.35% (v7.3).

## Slide 11
AI Vision — Four Approaches, One Winner
▦ [Diagram Request: four status cards in a row — ❌ / ❌ / ⚠️ / ✅ — the 4th (Depthwise-separable RGB) highlighted in teal with a ✓ tick; optional small "accuracy vs latency" quadrant with ★ v7.16 sitting in the sweet spot (high accuracy + low latency).]
We tried four model families to satisfy accuracy + latency + from-scratch all at once on the ESP32-CAM. Only the last cleared all three.
1 · Simple CNN — standard convolutions, from-scratch ❌ — couldn't generalize: overfit on ~1k images, human recall only 67–76% (and the heavier versions were also slow). Low capacity ≠ robust.
2 · Knowledge distillation — big teacher → tiny student ❌ — strong on paper (91.77%), but the student stayed 48×48 grayscale, so it hit the same real-scene detail ceiling; extra training complexity for no real-world gain.
3 · Pre-trained transfer — MobileNetV1 0.2 ⚠️ — most accurate (92.35%) but too slow (~1 s) on the ESP32, and a borrowed ImageNet backbone → weak novelty for the FYP.
4 · Depthwise-separable, from-scratch, RGB ✅ ★ — the winner (v7.16): depthwise factorization cut conv MACs ~8–10× → light enough to run from-scratch sub-second (~872 ms); RGB at 96×96 kept the colour/detail grayscale strips out (≈ +5–7 pts human recall). 90.83%, balanced, custom.
Why it finally worked (one line): depthwise-separable makes a from-scratch network light enough to be fast, and RGB at 96×96 makes it detailed enough to generalize — the one combination that hit all three constraints at once.
Notes: Visuals to add:
- [Diagram Request: four status cards in a row — ❌ / ❌ / ⚠️ / ✅ — the 4th (Depthwise-separable RGB) highlighted in teal with a ✓ tick; optional small "accuracy vs latency" quadrant with ★ v7.16 sitting in the sweet spot (high accuracy + low latency).]

## Slide 12
AI Vision — Final Technique (Deep Dive): Depthwise-Separable, From-Scratch
▦ [Diagram Request: Vertical Layer Stack Diagram]
Input 96×96×3 RGB → Conv2D(8) +BN +MaxPool → SeparableConv2D(16) +BN +MaxPool → SeparableConv2D(32) +BN +MaxPool → Flatten → Dropout(0.5) → Dense(2, Softmax)
Why depthwise-separable: each standard convolution is factorized into a depthwise (per-channel) conv + a 1×1 pointwise conv → ~8–10× fewer multiply-accumulates. Conv MACs ≈ 2.8M (v7.16) vs ~17–42M for standard convs — this is what makes a from-scratch CNN fit the ESP32 budget and stay sub-second.
From-scratch (no borrowed backbone): satisfies the FYP novelty requirement — a custom architecture the team owns, not a pretrained MobileNet, that still clears >90%.
ESP-NN disabled (on-device bias fix): ESP-NN is Espressif's neural-network kernel library — hand-optimized low-level conv / depthwise / pooling routines that accelerate TensorFlow Lite Micro inference on the ESP32. Here its depthwise kernel saturated the model to "always human" on the ESP32-S1 (the v7.14 bug); turning ESP-NN off (falling back to the reference kernels) removed the bias with no accuracy loss — the model is light enough to stay sub-second even without the accelerator.
Balanced training: 929 human / 920 non-human + class weights → no class bias.
INT8 quantization: input scale 1/255 (zero-point −128), output scale 1/256 — the same calibration as the EI "final" pipeline; deployed as model_data.h.
Resolution as the final lever: bumping 80×80 → 96×96 (v7.15 → v7.16) added the last ~2.5 pts needed to cross 90%.
Notes: Visuals to add:
- [Diagram Request: Vertical Layer Stack Diagram]

## Slide 13
AI Vision — Results
▦ [Visual Request: Comparison bar chart — Test Accuracy & Human Recall for v7.16 vs v7.15 vs v7.3]
Final deployed model — ★ v7.16 (96×96 RGB depthwise, from-scratch, ESP-NN off):
Held-out TEST accuracy 90.83% (297/327) — the >90% target met.
Human recall 87.5% (98/112) · non-human recall 92.6% (199/215) — balanced, no class bias.
On-device latency ~872 ms on the ESP32-CAM — fully local, INT8, no GPU, no cloud.
From-scratch depthwise CNN (~2.8M conv MACs); ESP-NN off → no on-device saturation (runs cleanly, no bias).
Two predecessors, for context:
v7.15 (80×80 RGB depthwise, ESP-NN off) — the direct predecessor: balanced 88.38% test (human/non-human recall both 88.4%). Proved depthwise + RGB + ESP-NN-off fixed the on-device bias; v7.16 then bumped 80→96 for the last ~2.5 pts.
v7.3 (96×96 RGB MobileNetV1, class-weighted) — the project's peak accuracy 92.35% test (human recall 92.0%), but on a borrowed ImageNet backbone. v7.16 deliberately traded ~1.5 pts to be fully from-scratch (novelty) while staying balanced and ESP-NN-safe.
Model | Architecture | Input | Test acc | Human recall | Note
v7.3 | MobileNetV1 0.2 (transfer) | 96×96 RGB | 92.35% | 92.0% | peak — borrowed backbone
v7.15 | Depthwise, from-scratch | 80×80 RGB | 88.38% | 88.4% | direct predecessor
★ v7.16 | Depthwise, from-scratch | 96×96 RGB | 90.83% | 87.5% | deployed final
Notes: Visuals to add:
- [Visual Request: Comparison bar chart — Test Accuracy & Human Recall for v7.16 vs v7.15 vs v7.3]

## Slide 14
Backend Integration (Gateway & Cloud)
▦ [Visual Request: Python Terminal Output showing Magic Byte verification]
MQTT Protocol: Uses lightweight publish/subscribe model (eagleeye/camera/image) to save battery.
Python Bridge (Gateway):
  Acts as a security buffer (the camera has no direct internet access).
  Verifies JPEG "Magic Bytes" to ensure data integrity before upload.
  Handles secure API handshakes with Cloudinary and Firebase.
Notes: Visuals to add:
- [Visual Request: Python Terminal Output showing Magic Byte verification]

## Slide 15
Mobile Application
▦ [Visual Request: App Screen & Alert Notification]
Technology: React Native (Expo).
Key Features:
  Real-time Sync: Gallery updates instantly via Firebase listeners.
  Visual Evidence: Fetches high-res secure URLs from Cloudinary.
  System Health: Displays connection status and last-seen timestamps.
Notes: Visuals to add:
- [Visual Request: App Screen & Alert Notification]

## Slide 16
Results & Performance Analysis (System)
Latency Metrics (end-to-end):
  On-device detection: ~872 ms (ESP32-CAM, v7.16 — fully local, no cloud/GPU).
  Upload: ~2-3s (Network dependent).
  Alert to phone: < 1s (App).
Detection accuracy: 90.8% held-out test, balanced (87.5% human / 92.6% non-human recall) — detail in "AI Vision — Results".
Stability: Decoupled architecture prevents the camera from freezing during network uploads.

## Slide 17
Revised Work Division
▦ [Visual Request: Table/Chart showing roles]
Murtaza Khalid (Computer Vision & Embedded AI):
  Dataset & Training: Curated the human detection dataset and trained the custom TinyML model (Int8 Quantized).
  Firmware Development: Developed the ESP32-CAM C++ firmware, optimizing the inference engine and camera driver.
  State Machine Logic: Implemented the "Warm-up" and "Cooldown" algorithms to eliminate false positives.
Haseeb (Audio Intelligence & Sensing):
  Audio Model Development: Trained the Audio Classification Model on urban sound datasets (UrbanSound8K).
  Threat Detection: Optimized the model to specifically detect "Door Opening", "Footsteps", and "Glass Breaking".
  Integration: Tuned the inference to run within 300ms latency for real-time acoustic alerts.
Huzaifa Khan (IoT Connectivity & Mobile App):
  Backend Architecture: Designed the secure Python Gateway, MQTT Broker, and Cloud integrations (Cloudinary/Firebase).
  Mobile App: Built the React Native application for real-time alerts, live streaming, and history retrieval.
  System Security: Implemented Magic Byte verification and secure API handshakes.
Notes: Visuals to add:
- [Visual Request: Table/Chart showing roles]

## Slide 18
Societal Impact & Sustainability (UN SDGs)
▦ [Visual Request: Icons of SDG 9, SDG 11, and SDG 16]
Alignment with UN Sustainable Development Goals:
  SDG 9 (Industry, Innovation & Infrastructure): Democratizing access to AI security by using low-cost, readily available microcontrollers (~$10 vs $200+ systems).
  SDG 11 (Sustainable Cities & Communities): Enhancing safety in low-income housing where expensive security systems are unaffordable.
Privacy & Ethics:
  Privacy by Design: Images are processed locally. Only confirmed threats are transmitted. Empty frames or non-threats never leave the device, preserving user privacy.
Notes: Visuals to add:
- [Visual Request: Icons of SDG 9, SDG 11, and SDG 16]

## Slide 19
Updated Timeline & Milestones
(Mapping: Rubric MR5 - Revised Milestones)
▦ [Visual Request: Gantt Chart]
Completed:
  ✅ AI Vision: Confirmed as finished (Human Detection).
  ✅ Voice Integration: Confirmed as finished (Alerts).
  ✅ Core System: Confirmed as finished (Live Stream & Arming).
Upcoming (Final Phase):
  ⬜ Dynamic Control: Pan/Tilt & Auto-Tracking.
  ⬜ Physical Security: Door Lock Integration.
  ⬜ Final Steps: System Integration Testing.
Notes: Visuals to add:
- [Visual Request: Gantt Chart]

## Slide 20
Conclusion
Summary: EagleEye proves that sophisticated "Smart Security" does not need expensive hardware.
Key Achievement: Runs a custom, from-scratch 96×96 RGB depthwise-separable CNN fully on-device (~872 ms, 90.8% balanced accuracy) while maintaining a cloud-connected, user-friendly mobile app.
Future Scope: Exploring solar power integration and "Face Recognition" add-ons.

## Slide 21
Q&A
Thank You.
Open for Questions.

## Slide 22
References (IEEE)
[1] M. A. Al-Khedher, "Hybrid Vision-Based Surveillance System for Smart Home Applications," IEEE Transactions on Consumer Electronics, vol. 65, no. 4, pp. 450-459, 2019.
[2] S. Tanwar et al., "Privacy-Preserving Surveillance Using Edge Computing," 2020 IEEE International Conference on Computing, Power and Communication Technologies (GUCON), 2020.
[3] P. Warden, "TinyML: Machine Learning with TensorFlow Lite on Arduino and Ultra-Low-Power Microcontrollers," O'Reilly Media, 2019.