## Slide 1
04
LITERATURE REVIEW & ANALYSIS
INTRODUCTION
A systematic review across the project's domains — surveillance, on-device vision, model compression, IoT & sensing — with the gap each leaves open.
THEME | KEY WORKS | WHAT THE LITERATURE SHOWS | GAP → OUR OPPORTUNITY
Cloud / commercial cameras | Ring, Nest; Al-Khedher [1] | Continuous cloud streaming enables smart alerts. | Privacy risk, high bandwidth, recurring fees.
Edge & privacy computing | Shi et al. [2]; Tanwar et al. [3] | Moving compute to the edge cuts latency & exposure. | Most still offload inference; few run fully on-device.
Detection models | YOLO [4], SSD [5] vs MobileNet [6][7] | Accurate detectors exist; depthwise-separable conv is far lighter. | Heavy nets exhaust 520 KB SRAM (1–3 FPS, brownouts); light nets target phones, not a ~100 KB MCU.
Model compression | INT8 quant. [8], distillation [9] | ~4× smaller models with integer-only math. | A real quantization gap; tiny models lose generalization.
TinyML on MCUs | Warden [10]; TFLite-Micro [11] | OS-free, low-latency inference on bare metal. | Mostly research demos, not privacy-first product systems.
Sensing & connectivity | PIR motion; MQTT [12]; UrbanSound8K [13] | Cheap triggers; lightweight pub/sub; urban-sound classification. | PIR alone = 85–95% false alarms; MQTT demos are LAN-only; audio rarely fused with vision.
RESEARCH GAP — the synthesis
No low-cost system combines (a) fully on-device human detection for privacy, (b) outbound-only cloud access that works on any network without port-forwarding, and (c) audio threat fusion — on a ~$10 microcontroller. EagleEye targets exactly this gap.

## Slide 2
05
FOUNDATIONS WE BUILD ON
INTRODUCTION
We don't just cite these techniques — we benchmarked and adapted them (18 model variants; see "AI Vision").
🧩
Depthwise-separable convolutions [6][7]
Factorize conv into depthwise + 1x1 pointwise -> ~8–10x fewer MACs. → Enables our from-scratch on-device CNN (v7.16) based on MobileNet structure.
⚙️
INT8 post-training quantization [8]
32-bit -> 8-bit. ~75% smaller; integer-only math. → Fits the ~100 KB tensor arena. Quantizes both weights & input pixels (Scale & Zero-Point).
🎓
Knowledge distillation [9]
Transfer knowledge from a large teacher model to a small student model. → Evaluated (v4.0, 91.77%); informed our capacity & resolution choices.
🛠️
TFLite-Micro on bare metal [10][11]
OS-free, low-latency inference directly on microcontrollers. → Runs on ESP32-CAM. Accelerated by ESP-NN assembly kernels (3x speedup, 2.5s -> 0.8s).
🔒
Edge / privacy-by-design [2][3]
Analyze locally on-chip; never stream raw video to the cloud. → Transmit only confirmed human threat snapshots for alerts.
📡
MQTT pub/sub [12] + UrbanSound8K [13]
Lightweight pub/sub network messaging combined with audio classification. → Outbound-only cloud alerts + triggers from our audio threat detector.
POSITIONING
EagleEye combines these proven building blocks into a single privacy-first, remotely-accessible edge device — and contributes a custom from-scratch depthwise-separable detector that holds >90% accuracy entirely on-device.

## Slide 3
09
ESP32 CHIP ARCHITECTURE & MEMORY MAP
FIRMWARE
FLASH (4 MB)
Firmware code
Model: 13 KB
  • architecture
  • weights
ESP-NN library code
  • optimized C for conv, dense, pool
  • replaces generic TFLite math (3× faster)
INTERNAL SRAM (~520 KB)
Tensor Arena (126 KB)
  • conv outputs live here (reused every layer)
snapshot_buf (27 KB)
  • 96×96 RGB888 image buffer
TLS session (40 KB)
  • MQTT encryption overhead
FreeRTOS + WiFi (~150 KB)
  • operating system & network stack
PSRAM (4 MB)
Camera buffer 1 (150 KB)
Camera buffer 2 (150 KB)
  • dual-buffered DMA camera capture
HARDWARE
LEDC PWM → controls pan/tilt servos
DMA → high-speed camera data transfer
Radio → WiFi antenna signal
CPU
Core 0: servo stepper task (330Hz) | WiFi driver & stack
Core 1: camera capture → resize → normalize → conv(ESP-NN) → pool(ESP-NN) → sepconv(ESP-NN) → pool(ESP-NN) → sepconv(ESP-NN) → pool → dense(ESP-NN) → decision

## Slide 4
10
MODEL ACCELERATION & SPEED OPTIMIZATION
MODEL
1. ESP-NN Library Optimization
Hardware-Level Assembly Kernels
Replaces standard TFLite math loops
  • Replaces generic C code with hand-optimized assembly routines from Espressif.
Targets key pipeline layers
  • Optimizes Conv2D, MaxPool, DepthwiseConv, and Fully Connected operations.
Xtensa LX6 SIMD Instructions
  • Executes multiple math operations simultaneously per CPU clock cycle.
Massive Speedup Result
  • Reduces inference time from 2.5s down to 800ms (3× speed boost).
2. INT8 Quantization
Integer Math Conversion
Converts weights & activations
  • Drops model float values from 32-bit floats to signed 8-bit integers.
Bypasses FPU hardware limit
  • ESP32 lacks double-precision FPU; float operations require slow software emulation.
Single-cycle ALU operation
  • Integer additions and multiplications run natively in single clock cycles.
Saves critical Flash space
  • Quantized model weighs 13 KB instead of 52 KB (75% memory footprint reduction).
3. Depthwise Separable Convs
Architectural Layer Design
Decomposes standard convolutions
  • Splits standard 2D convs into 2 distinct operations: Depthwise and Pointwise.
Depthwise step (3x3 filter)
  • Filters input channels individually (applies spatial filter channel-by-channel).
Pointwise step (1x1 projection)
  • Linearly combines outputs across all channels to build final features.
9x Reduction in MAC Math
  • Drastically cuts parameters and CPU operations with minimal accuracy loss.