## Slide 1
10
AI MODEL OPTIMIZATION & SPEEDUP FACTORS
FIRMWARE
1. INT8 QUANTIZATION
Precision Downsizing
What it is:
  Converts weights & activation floats (32-bit) to integers (8-bit) post-training.
Key Benefits:
  • Shrinks model size 4× (from 52 KB to 13 KB), allowing it to easily fit in the internal Flash.
  • Reduces memory bandwidth requirement, preventing bottlenecks.
  • Replaces costly floating-point calculations with faster, native integer arithmetic.
2. DEPTHWISE SEPARABLE CONV
Algorithmic Efficiency
What it is:
  Splits standard 2D convolution into a spatial filter (Depthwise) and a channel mixer (Pointwise).
Key Benefits:
  • Mathematically reduces total multiplications by ~80-90% for a 3x3 kernel.
  • Total operations drop from tens of millions to only 3.2 million multiply-adds.
  • Significantly reduces memory footprint needed for intermediate tensors.
3. ESP-NN ACCELERATION
Hardware-Specific Kernels
What it is:
  Espressif's library containing hand-tuned assembly/C kernels optimized for the Xtensa processor.
Key Benefits:
  • Replaces default, generic TensorFlow Lite Micro mathematical operations.
  • Implements SIMD-like instruction usage to run multiple multiplications per clock cycle.
  • Performance boost: Reduces inference time 3× (from ~2.5 seconds down to 800 milliseconds).