## Slide 1: EagleEye: Intelligent Edge AI Surveillance System
I N F O R M A T I O N T E C H N O L O G Y U N I V E R S I T Y · L A H O R E
Final Year Project — Final Defence
P R E S E N T E R S
Murtaza Khalid (BSCE22004) · Huzaifa Khan (BSCE22025) .
Muhammad Haseeb (BSCE22048)
S U P E R V I S I O N
Dr. Rehan Hafiz (Professor) · Dr. Rehan Ahmed (Asst. Professor & Chairperson)
Chairperson)
D E P A R T M E N T
Computer & Software Engineering, Faculty of Engineering, ITU Lahore
D E F E N C E
Final Year Project — June 2026
June 2026

## Slide 2: Introduction
01
P A R T O N E
The problem, the gap, and the privacy-first solution we propose.

## Slide 3
01
Dataset Collection
\

## Slide 4: 02 PROBLEM STATEMENT
I NTRODUCTI ON
The issue
Traditional surveillance is video and bandwidth-heavy, expensive and privacy-
privacy-invasive —24/7 streamed to the cloud.
The gap
Few affordable, privacy-first smart cameras process data on edge.
Our goal
A decentralized, low-power system that detects intruders locally on an ESP32-CAM and transmits only confirmed threats.

## Slide 5: 03 PROPOSED SOLUTION & CORE FUNCTIONALITIES
I N T R O D U C T I O N
A proactive, multi-layered security system combining Edge AI with physical automation.
AI Vision Detection
Real-time human recognition with TinyML — no motion false alarms.
Voice Alert System
Audible warning on detection to deter intruders.
Live Surveillance
Low-latency streaming for manual verification.
Dynamic Camera Control
Manual remote pan/ tilt from the app

## Slide 6: 04 PROPOSED SOLUTION & CORE FUNCTIONALITIES
I N T R O D U C T I O N
A proactive, multi-layered security system combining Edge AI with physical automation.
cam
Oled display
esp32
Servo sg90
Pir sensor

## Slide 7: 05 LITERATURE REVIEW & ANALYSIS
I N T R O D U C T I O N
A systematic review across the project's domains — surveillance, on-device vision, model compression, IoT & sensing — with the gap each leaves open.
THEME | KEY WORKS | WHAT THE LITERATURE SHOWS | GAP → OUR OPPORTUNITY
Cloud / commercial cam eras | Cloud | Continuous cloud streaming enables smart alerts. | Privacy risk, high bandwidth, recurring fees.
Edge & privacy computing | Edge devices | Moving compute to the edge cuts latency & exposure. | Most still offload inference; few run fully on-device.
Detection models | YOLO , SSD vs MobileNet | Accurate detectors exist; depthwise-separable conv is far lighter. | Heavy nets exhaust 520 KB SRAM (1–3 FPS, brownouts); light nets target phones, not a ~100 KB MCU.
Model compression | INT8 quant, distillation | ~4× smaller models with integer-only math. | A real quantization gap; tiny models lose generalization.
Hardware-optimized libraries | CMSIS-NN , ESP-NN; TFLite-Micro | CPU-specific assembly kernels yield 3–5× speedup; OS- free inference runtime. | Few combine custom kernels with on-device CNN on a ~$10 MCU.
Sensing & connectivity | PIR motion; MQTT | Cheap triggers; lightweight pub/sub; urban-sound classification. | PIR alone = 85–95% false alarms; MQTT demos are LAN-only; audio rarely fused with vision.

## Slide 8: 06 FOUNDATIONS WE BUILD ON
I NTRODUCTI ON
We don't just cite these techniques we benchmarked and adapted them(18 model variants; see “AI Vision”).
Depthwise-separable convolutions
Factorize conv into depthwise + 1×1 pointwise → ~8–10× fewer MACs.
→ Enables our from-scratch on-device CNN (v7)
INT8 post-training quantization
32-bit → 8-bit · ~75%smaller · integer-only math.
→ Fits the ~126KB tensor arena.
Hardware-optimized kernels
CPU-specific assembly (ESP-NN / CMSIS-NN) replaces generic C → 3–5× speedup.
→ Accelerates inference on the ESP32’s Xtensa LX6 cores.
Edge / privacy-by-design
Analyze locally; never stream raw video.
→ Transmit only confirmed threats.
FREERTOS
Use freeRtos for multiple tasks
-> enables use to control servo smoothly

## Slide 9: The System
02
P A R T T W O
End-to-end architecture — from the ESP32-CAM edge to the mobile app.
app.

## Slide 10: 07 SYSTEM ARCHITECTURE — v1: LOCAL PROTOTYPE
T H E S Y S T E M
One network for everything — a PC must stay powered on at the site.
CLOUD
Cloudinary
image evidence (JPEG)
Firebase
alert metadata · config/armed
LAN · one Wi-Fi network — phone, camera & PC all here
ESP32-CAM
camera +TinyML
SITE PC
Mosquitto broker · bridge.py uploader
must stay powered ON
Phone (app)
React Native · same LAN
MQTT
app reads Firebase
✕ Live video (MJPEG) + servo — app must type the camera's LAN-IP directly
WHY v1 ISN'T SHIPPABLE
✕ Same network only — phone must be on the site Wi-Fi
✕ A PC must stay ON running Mosquitto + bridge.py
✕ Type the camera's IP — breaks on CGNAT / no port-forwarding
✕ Open broker · no TLS · hard-coded Wi-Fi credentials

## Slide 11
08
SYSTEM ARCHITECTURE — v2: CLOUD & OUTBOUND-ONLY
THE SYSTEM · CURRENT ★
The device dials OUT and stays connected — works from any network: no IP, no port-forwarding, no PC on site.
SITE A
any network
CLOUD
managed services
ANYWHERE
phone, on or off Wi-Fi
ESP32-CAM
HiveMQ Cloud — MQTT/TLS broker
topics: status·LWT · alert · cmd · ack
Cloudinary — image evidence
device HTTPS-POSTs the JPEG
Firebase → Cloud Function
push fires even with the app closed
Deno Deploy — WebSocket relay
on-demand video · never 24/7
Phone (app)
MQTT-over-WebSocket
🔒
🔒
🔒
🔒
🔒
THE KEY IDEA · OUTBOUND-ONLY
✓ Camera always connects OUT (like a messaging app) — no static IP, no port-forwarding, no on-site PC
✓ TLS everywhere (mqtts 8883 · wss · HTTPS) · per-device credentials · least-privilege topics
🔒
🔒

## Slide 12
09
ENGINEERING — INSIDE THE ESP32
T H E S Y S T E M
EagleEye · FYP Final Defence · June 2026
11 / 28
ESP32 CHIP
FLASH (4 MB)
Firmware code
Model
├ architecture
└ weights
ESP-NN library code
└ optimized C for conv, dense, pool
(replaces generic TFLite math, 3× faster)
INTERNAL SRAM (~520 KB)
Tensor Arena
└ conv outputs live here
└ reused every layer
snapshot_buf
└ 96×96 RGB888 image
TLS session
└ MQTT encryption
FreeRTOS + WiFi
weights loaded
PSRAM (4 MB)
Camera buffer 1 (150 KB)
Camera buffer 2 (150 KB)
CPU
Core 0: servo stepper (330 Hz) · WiFi driver
Core 1: camera → resize →
normalize → conv(ESP-NN) → pool(ESP-NN) →
sepconv(ESP-NN) → pool(ESP-NN) →
sepconv(ESP-NN) → pool → dense(ESP-NN) → decision
Other operations also happens here
HARDWARE
LEDC PWM → servos
DMA → camera
Radio → WiFi antenna

## Slide 13
10
ENGINEERING — AI OPTIMIZATION
T H E S Y S T E M
EagleEye · FYP Final Defence · June 2026
12 / 28
Three Pillars of AI Optimization: How We Achieve 3× Faster Inference on ESP32
1
ESP NN Kernels
Hardware-level Speed
WHAT IT IS
Optimized math routines written by Espressif (ESP32 manufacturer) specifically for neural network inference.
HOW IT HELPS
Replaces generic TFLite C code with hand-tuned assembly instructions designed for the ESP32 CPU architecture.
Accelerates core operations:
conv · dense · pool · sepconv
RESULT: 2.5 s → 0.8 s (3× speedup)
2
INT8 QUANTIZATION
Integer Math for Model & Image
WHAT IT IS
Convert all numbers — weights, activations, and input pixels — from float32 to signed int8 (−128 to 127).
IMAGE QUANTIZATION PIPELINE
1. Camera captures raw RGB (0–255)
2. Normalize to floats (0.0–1.0)
3. Convert to int8 via Scale & Zero-Point
WHY IT MATTERS
ESP32 has no float hardware — decimal math is very slow. Int8 runs natively in a single CPU cycle.
Model shrinks 75%: 52 KB → 13 KB
RESULT: 100% integer math — zero float bottlenecks
3
DEPTHWISE SEPARABLE
Architectural Math Reduction
WHAT IT IS
Split standard 2D convolutions into two simpler, sequential steps:
Depthwise → Pointwise (1×1)
HOW IT HELPS
Depthwise: filters spatial features independently per channel.
Pointwise: merges channels using a 1×1 convolution filter.
Massively fewer multiply-accumulate operations vs standard conv.
RESULT: ~9× fewer calculations, minimal accuracy loss

## Slide 14: AI Vision
03
P A R T T H R E E · C O R E T E C H N I C A L C O N T R I B U T I O N
17 engineered variants, five phases, one constraint: it must run on the ESP32-CAM
itself.

## Slide 15
11
AI VISION — FOUR APPROACHES, ONE WINNER
AI VISION
We tested four model families against three hard constraints on the ESP32-CAM — accuracy, latency & from-scratch. Only the last cleared all three.
APPROACH
ACCURACY
LATENCY
FROM-SCRATCH
VERDICT
Simple CNN
standard convolutions
✗
67–76% recall
overfit on ~1k imgs
✗
slow when scaled
heavy variants >300 ms
✓
fully custom
built from scratch
Low capacity ≠ robust — can't generalize.
Knowledge Distillation
big teacher → tiny student
✗
91.77%
Highly latent
student stays small
✗
needs a teacher
extra train complexity
We tested it but did not performed well on esp
Pre-trained Transfer
MobileNetV1 0.2 backbone
✓
92.35%
most accurate of all
✗
~1 s
too slow on ESP32
✗
borrowed
ImageNet backbone
Accurate, but slow & weak novelty.
Depthwise-Separable RGB
from-scratch · 96×96 · v7.16
✓
90.83%
balanced & robust
✓
~872 ms
sub-second, on-device
✓
custom & novel
depthwise factorized
★ Cleared all three at once.
WHY IT FINALLY WORKED
Depthwise-separable factorization cuts conv MACs ~8–10× — light enough to run from-scratch sub-second (~872 ms); and RGB at 96×96 keeps the colour/detail grayscale dropped (≈ +5–7 pts recall) — detailed enough to generalize (90.83%). The one combination that satisfied all three constraints together.

## Slide 16
12
AI VISION — FOUR APPROACHES, ONE WINNER
AI VISION
Ver. | Architecture | Input | Accuracy¹ | Latency² | Verdict
PHASE 1 — SIMPLE CNN Low capacity — couldn’t generalize beyond lab images |  |  |  |  | 
P0 ref | Pretrained person detector (EI / TFLite) | ~96×96 | 70% | ~700 ms* | proved on-device TFLite; generic, not ours
v1.0 | Tiny separable CNN | 48×48 gray | 80–85% | ~106 ms | original prod; too weak very low human recall
v2.1 | Tiny CNN + hard negatives | 48×48 gray | >90% | ~1006 ms | field-hardened high latency
v3.0 | Heavy CNN 16-32-64 (Optuna) | 48×48 gray | 94.96% | >3000 ms | most accurate, not generalizable
v6.1 | Edge Impulse CNN | 96×96 gray | ~90% | ~5000 ms* | Too slow
PHASE 2 — KNOWLEDGE DISTILLATION 48px ceiling killed real-world gains |  |  |  |  | 
v4.0 | Distilled tiny (MobileNetV2 teacher) | 48×48 gray 96*96 rgb | 91.77% | >3000 ms | slow
PHASE 3 — PRE-TRAINED TRANSFER Most accurate, but too slow + weak novelty |  |  |  |  | 
v7.3 | MobileNetV1 0.2 (transfer) | 96×96 RGB | 92.35% (peak) | ~2 s* | most accurate (borrowed backbone)
v7.4 | MobileNetV1 0.2 + EON | 64×64 RGB | 91.13% | ~2000 ms | Low inference
PHASE 4 — DEPTHWISE-SEPARABLE ★ WINNER ★ Cleared >90 %, sub-second, fully custom |  |  |  |  | 
v7.15 | Depthwise-separable, from-scratch | 80×80 RGB | 88.38% | ~750 ms* | bias fixed; just under 90
★ v7.16 | Depthwise-separable, from-scratch | 96×96 RGB | 90.83% | ~872 ms | deployed final
v7.17 | Depthwise-separable (gray) | 96×96 gray | 86.24% | ~600 ms* | Not accurate
TAKEAWAY Each phase solved one problem but introduced another — only Phase 4 (depthwise-separable + 96×96 RGB + class balancing) cleared accuracy, latency, and novelty simultaneously.

## Slide 17: 13 AIVISION — TRAINING TECHNIQUES (THE TOOLBOX)
A I V I S I O N
INT8 Quantization
4× smaller, integer math on the MCU; calibrated on representative data.
Data Augmentation
Flips / rotation / zoom / brightness brightness for lighting & angle robustness.
Hard-Negative Mining
A live ESP32 Wi-Fi capturer harvested field mistakes; oversampled past 90%.
Optuna Search
Automated LR / dropout / architecture tuning.
Knowledge Distillation
MobileNetV2 teacher → tiny student (α=0.378, T=9.23) → 91.77%.
Class Balancing
Balanced class using augmenetation
Transfer Learning
Pretrained MobileNetV1 (96×96 RGB) → project peak 92.35%.
Final Lever: Resolution
80 → 96 added the last ~2.5 pts to cross 90%.

## Slide 18
14
CUSTOM DATASET — SUMMARY
DATA COLLECTION
THE KEY NUMBERS
 | Real | Augmented | Total
Human | 876 | 272 | 1,148
NonHuman | 1,148 | 0 | 1,148
Total | 2,024 | 272 | 2,296
3 COLLECTION SOURCES
ESP32-CAM
320×240, 7 sessions over 17 days
Hard Neg. Capturer
Human Sample
NonHuman Sample
Lightweight CNN on ESP32-CAM flags uncertain frames → manually labelled → injected back (active learning loop)

## Slide 19
15
AI VISION — FINAL TECHNIQUE · DEPTHWISE-SEPARABLE, FROM-SCRATCH
AI VISION
Why depthwise-separable
Each conv factorize into depthwise + 1×1 pointwise — roughly 8–10× fewer MACs. Total conv M ACs ≈ 2.8 M (vs 17–42 M), which fits the ESP32 and stays sub-second per inference.
From-scratch
No borrowed backbone. The novelty requirement is met with a custom architecture we own end-to-end, while still clearing >90% accuracy.
ESP-NN Enables
Esp-NN enable reduce latency
Balanced training + INT8
920 human / 920 non-human samples with class weights.
Custom CNN · ESP32-S3 · INT8 quantized
Slide 10 / 10

## Slide 20
16
AI VISION — FINAL MODEL RESULTS
AI VISION
90.83%
Test Accuracy
872 ms
On-Device Latency
87.5%
Human Recall
92.6%
NonHuman Recall
DETAILED METRICS
Metric | Human | NonHuman
Precision | 85.96% | 93.43%
Recall | 87.50% | 92.56%
F1 Score | 86.72% | 93.00%
Macro F1 | 89.86% | 
Weighted F1 | 90.85% | 
✓ >90% Accuracy (90.83%)
✓ Sub-Second (872 ms)
✓ Fully From-Scratch
EagleEye · FYP Final Defence · June 2026
Notes: Key points: (1) v7.16 achieves 90.83% test accuracy on 327 real images. (2) On-device inference at 872ms on ESP32-CAM. (3) Entirely from scratch. (4) Balanced recall: 87.5% Human, 92.6% NonHuman. (5) Only ~13 KB with full INT8 quantization.

## Slide 22
16
SYSTEM ARCHITECTURE
THE SYSTEM
EagleEye · FYP Final Defence · June 2026
1 / 5
INMP441
Microphone
Sound input
→
I2S Bus
(ESP32-CAM)
Digital transfer
→
MFCC
Processor
Feature extraction
→
TinyML
Engine
Classification
→
Alert
Output
Notification
HARDWARE SPECIFICATIONS
Microcontroller
ESP32-CAM (Xtensa LX6, 240 MHz)
Microphone
INMP441 — Omnidirectional MEMS
Interface
I2S Digital Protocol
Sampling Rate
16,000 Hz (16 kHz)
PSRAM
4 MB External (MFCC buffer)
SOFTWARE STACK
Framework
Arduino (ESP-IDF underneath)
ML Runtime
TensorFlow Lite Micro
Audio DSP
MFCC — 13 Coefficients
Connectivity
MQTT via Wi-Fi
Inference Mode
Continuous Sliding Window

## Slide 23
17
AUDIO FEATURE EXTRACTION
THE SYSTEM
EagleEye · FYP Final Defence · June 2026
2 / 5
MFCC PROCESSING PIPELINE
1
Audio Capture
INMP441 records mono audio at 16,000 Hz via I2S bus.
2
Framing & Windowing
Audio split into overlapping 25 ms frames with Hamming window.
3
FFT — Frequency Analysis
Fast Fourier Transform converts each frame to frequency spectrum.
4
Mel Filter Bank
40 triangular filters map spectrum to human auditory scale.
5
MFCC Coefficients
13 compact cepstral coefficients extracted per frame — model input.
MFCC PARAMETERS
Sampling Rate
16,000 Hz
Frame Length
25 ms
Frame Overlap
10 ms
FFT Size
512 points
Mel Filters
40 banks
Coefficients
13 per frame
Input Window
2,756 ms total
WHY MFCC FOR INTRUSION DETECTION?
✓ Mimics human auditory perception
✓ Robust against background noise
✓ Compact: 44,100 samples → 13 values
✓ Proven for embedded audio classification

## Slide 24
18
TINYML MODEL DESIGN
AI VISION
EagleEye · FYP Final Defence · June 2026
3 / 5
CLASSIFICATION OUTPUT CLASSES
Background
Ambient / No Threat
Normal environment sounds.
No action triggered.
Footsteps
Unauthorised Movement
Human movement detected.
Alerts pushed immediately.
Glass Break
Forced Entry Detected
High-frequency shatter event.
Critical alert triggered.
CNN MODEL ARCHITECTURE
Input Layer
13 MFCC × Time-steps
Conv1D + ReLU
32 filters, kernel size 3
MaxPooling1D
Pool size 2 — spatial reduction
Conv1D + ReLU
64 filters, kernel size 3
Flatten
Feature vector linearization
Dense (64)
Fully connected + ReLU
Softmax Output
3 classes — probability distribution
TRAINING CONFIGURATION
Optimizer
Adam (lr = 0.0005)
Loss Function
Categorical Cross-Entropy
Batch Size
32 samples
Epochs
100 with early stopping
Quantization
INT8 Post-training (TFLite)
Model Size
< 50 KB after quantization
93%
Accuracy
0.91
F1 Score
31 KB
RAM Used
87 ms
Inf. Speed

## Slide 25
19
REAL-TIME ON-DEVICE INFERENCE
THE SYSTEM
EagleEye · FYP Final Defence · June 2026
4 / 5
CONTINUOUS SLIDING WINDOW INFERENCE
Continuous Audio Stream (16,000 Hz)
Window 1 [0–2.7s]
Window 2 [0.7–3.4s]
Window 3 [1.4–4.1s]
Each window = 2,756 ms | Overlap = 50% | New result every 87 ms
INFERENCE CYCLE BREAKDOWN
1
Step 1 — Record
Capture 2,756 ms audio slice via I2S DMA
2
Step 2 — Extract
Compute 13 MFCC coefficients per frame
3
Step 3 — Classify
Run CNN forward pass on TFLite Micro runtime
4
Step 4 — Decide
Threshold check — confidence must exceed 70%
5
Step 5 — Publish
MQTT message sent to cloud broker if triggered
ON-DEVICE VS CLOUD PROCESSING
Metric
On-Device (Edge)
Cloud
Latency
< 100 ms
500 ms+
Internet
Not required
Required
Privacy
Audio local
Streamed
Cost
None
Recurring
Reliability
Always on
Depends on network
87 ms
Per Inference
100%
On-Device
0 ms
Network Latency

## Slide 26
20
DETECTION RESULTS & SYSTEM VALIDATION
RESULTS
EagleEye · FYP Final Defence · June 2026
5 / 5
SAMPLE INFERENCE OUTPUT — LIVE CLASSIFICATION
Background
8%
No Action
Footsteps
91%
ALERT TRIGGERED
Glass Break
1%
No Action
SYSTEM VALIDATION SUMMARY
Footsteps Detection
91.2% average confidence
Glass Break Detection
88.7% average confidence
Background Rejection
96.4% specificity
False Positive Rate
< 3.6% across test set
Detection Latency
87 ms from event to output
Continuous Operation
Stable over 8-hour test run
END-TO-END LATENCY BREAKDOWN
Audio Capture
2,756 ms (fixed window)
MFCC Extraction
83 ms
CNN Classification
4 ms
Threshold Decision
< 1 ms
MQTT Publish
< 50 ms (Wi-Fi)
Total (E2E)
< 3,000 ms — sub-3 second

## Slide 27
04
P A R T F O U R
Backend & App
The secure gateway, the cloud, and the app the user actually holds.

## Slide 28
21
CLOUD SERVICES & DATA FLOW
BACKEND & APP
Cloudinary — Photo Storage
\
Firebase — Alerts & Push
Deno Deploy — Video Relay

## Slide 29
22
MQTT COMMUNICATION
BACKEND & APP
HiveMQ Cloud is the message broker — 7 dedicated topics handle real-time state sync, alerts, commands, and video control.
BROKER CONNECTION
Detail | ESP32-CAM | Mobile App
Protocol | MQTT over TLS | MQTT over WSS
Port | 8883 | 8884
Client ID | eagle_eye_cam_01 | Auto-generated
Auth | Username + password | Username + password
LAST WILL & TESTAMENT (LWT)
On connect, ESP32 registers a will message:
Topic: {camId}/status Message: "offline"
QoS: 1 | Retain: true
If the camera loses power, HiveMQ auto-publishes "offline" — the app shows camera as offline instantly.
CAMERA PUBLISHES (4 topics)
{camId}/status | online / armed / disarmed — QoS 1, retained
{camId}/alert | Person detected → uploads photo → publishes secure_url
{camId}/detection_status | person_detected or no_person after each inference
{camId}/motor_status | left / right / center — confirms pan command executed
APP PUBLISHES (3 topics)
{camId}/command | arm or disarm — camera enables/disables detection
{camId}/stream_status | start or stop — camera opens/closes WebSocket relay
{camId}/pan | left / right / center — camera moves servo motor
Per-Camera Isolation Every topic prefixed with cameraId — multiple cameras share one broker, zero collision.
Per-Camera Topic Isolation
Retained + QoS 1 for /status
MQTT: ~30 KB RAM on ESP32

## Slide 30
23
SECURITY & SESSION MANAGEMENT
BACKEND & APP
All connections use TLS encryption. Separate credentials per service. The system self-heals on connection drops.
Encryption
All 7 connections (MQTT, HTTPS, WSS) are TLS-encrypted — zero plaintext traffic
ESP32 embeds the ISRG Root X1 CA certificate in flash
Validates the server's certificate chain before connecting — prevents MITM attacks even on untrusted Wi-Fi
Authentication
HiveMQ: separate credentials — eagle_eye_cam (camera) and eagle_eye_app (mobile) prevent single-breach compromise
Cloudinary: unsigned upload preset — no API secret stored on ESP32 firmware
Firebase: secure API key (ESP32) + official SDK (app); security rules restrict writes to /cameras/{camId}/ path
Deno Room Security: Implemented WebSocket room authentication using camera-specific access tokens. Only clients verified with valid identifiers can access the active live-feed room, preventing unauthorized stream interception.
Session & Self-Healing
LWT: camera registers "offline" will message — broker auto-publishes if camera crashes
MQTT Keep-Alive: app sends 30-second background pings to the broker
Auto-Reconnect: both ESP32 and app run background loops to re-establish connections and re-subscribe
Clean Session: app uses cleanSession: true — broker discards stale queued messages
Deno Room Cleanup: rooms created dynamically, deleted when both sides disconnect
No Open Ports
Both camera and phone connect outward. No port forwarding needed.
No Secrets on Hardware
Cloudinary uses unsigned preset; API secret never leaves the dashboard.
Self-Healing
LWT + auto-reconnect: system recovers from drops in seconds.

## Slide 31
24
MOBILE APPLICATION
BACKEND & APP
One app — built with React Native (Expo) — to watch, get alerted, and control the camera from anywhere.
Live status (MQTT)
HiveMQ MQTT-over-WebSocket for real-time status & commands.
Live view (Deno)
App tell whether esp32 cam is live or not
Honest status (LWT)
MQTT last-will gives a true online/offline indicator, not a guess.
Private & secure
Encrypted (TLS). Phone never connects directly to the camera.

## Slide 32: SOCIETAL IMPACT & SUSTAINABILITY (UN SDGS)
2 5
R E S U L T S
SDG 9 — Industry & Innovation
D em ocratising AI security on ~ $5 m icrocontrollers (vs $200+ systems).
SDG 11 — Sustainable Cities
Safer low- income housing where commercial security is
unaffordable.
SDG 16 — Privacy by Design
Images processed locally; only confirm ed threats ever leave the device.

## Slide 33: TIMELINE & MILESTONES
2 6
R E S U L T S
AI Vision — on-device human detection
COMPLETED
Voice alerts — TTS / siren deterrent
COMPLETED
Core system — live stream & smart arming
COMPLETED
Remote live video & camera pan/tilt
COMPLETED
Door-lock control — physical actuation
Full system integration testing
COMPLETED
COMPLETED

## Slide 34
27
PUBLIC HEALTH & SAFETY CONSIDERATIONS
S T A N D A R D S
ELECTRICAL & HARDWARE SAFETY
• 5V operation
• CPU thermal load
PRIVACY & DATA PROTECTION
• On-device AI processing
• Cloud photo storage
• MQTT control channel
NETWORK & CYBERSECURITY
• Internet-connected device outbound-only architecture, no inbound ports, no port-forwarding
• Stored WiFi credentials
USER WELLBEING & ETHICS
• Surveillance discomfort user arm/disarm control
12 identified hazards · 15 international standards referenced · Privacy-by-design · Outbound-only · All mitigations implemented in code
EagleEye · FYP Final Defence · June 2026
11 / 28

## Slide 35: WORK DIVISION
28
R E S U L T S
Murtaza Khalid
COMPUTER VISION & EMBEDDED AI
Dataset + TinyML training (INT8).
ESP32-CAM C++ firmware & inference engine
Muhammad Haseeb
AUDIO INTELLIGENCE & SENSING
Audio classifier on UrbanSound8K.
Detects door-open / footsteps / glass- break.
Huzaifa Khan
IOT CONNECTIVITY & MOBILE APP
Secure, MQTT, Cloudinary / Firebase.
React Native app.

## Slide 36
05
P A R T F I V E
Results & Wrap-up
System performance, contributions, impact, and what comes next.

## Slide 37: CONCLUSION
18
W R A P - UP
Summary
Sophisticated smart security does not need expensive hardware.
Key achievement
A custom , from - scratch 96× 96 RGB depthwise- separable C N N running device (~ 872 m s, 90.8% balanced accuracy), with a cloud - connected
that works from anywhere.
Future scope
Solar power; on-device face-recognition add-on.
90.8 %
balanced on-device accuracy
~872 ms
fully local inference
~$10
microcontroller hardware

## Slide 38: EagleEye
Smart AI surveillance, from anywhere.
Open for questions.

## Slide 39
20
REFERENCES (IEEE)
WRAP-UP
[1]
M. A. Al-Khedher, "Hybrid Vision-Based Surveillance System for Smart Home Applications," IEEE Trans. Consumer Electronics, vol. 65, no. 4, pp. 450–459, 2019.
[2]
W. Shi, J. Cao, Q. Zhang, Y. Li, and L. Xu, "Edge Computing: Vision and Challenges," IEEE Internet of Things Journal, vol. 3, no. 5, pp. 637–646, 2016.
[3]
S. Tanwar et al., "Privacy-Preserving Surveillance Using Edge Computing," in Proc. 2020 IEEE GUCON, 2020.
[4]
J. Redmon, S. Divvala, R. Girshick, and A. Farhadi, "You Only Look Once: Unified, Real-Time Object Detection," in Proc. IEEE CVPR, 2016, pp. 779–788.
[5]
W. Liu et al., "SSD: Single Shot MultiBox Detector," in Proc. ECCV, 2016, pp. 21–37.
[6]
A. G. Howard et al., "MobileNets: Efficient Convolutional Neural Networks for Mobile Vision Applications," arXiv:1704.04861, 2017.
[7]
M. Sandler, A. Howard, M. Zhu, A. Zhmoginov, and L.-C. Chen, "MobileNetV2: Inverted Residuals and Linear Bottlenecks," in Proc. IEEE CVPR, 2018, pp. 4510–4520.
[8]
B. Jacob et al., "Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference," in Proc. IEEE CVPR, 2018, pp. 2704–2713.
[9]
G. Hinton, O. Vinyals, and J. Dean, "Distilling the Knowledge in a Neural Network," in NIPS Deep Learning Workshop, 2015.
[10]
L. Lai, N. Suda, and V. Chandra, "CMSIS-NN: Efficient Neural Network Kernels for Arm Cortex-M CPUs," arXiv:1801.06601, 2018.
[11]
R. David et al., "TensorFlow Lite Micro: Embedded Machine Learning for TinyML Systems," in Proc. Machine Learning and Systems (MLSys), vol. 3, 2021, pp. 800–811.
[12]
A. Banks and R. Gupta, "MQTT Version 3.1.1," OASIS Standard, 2014.
[13]
J. Salamon, C. Jacoby, and J. P. Bello, "A Dataset and Taxonomy for Urban Sound Research," in Proc. ACM Int. Conf. Multimedia (ACM MM), 2014, pp. 1041–1044.